## Slide 1: Post-Silicon Verification using Quick Error Detection
ECE 7502 Class Discussion
Ben Calhoun
Thursday January 22, 2015

## Slide 2
Requirements
Specification
Architecture
Logic / Circuits
Physical Design
Fabrication
Manufacturing Test
Packaging Test
PCB Test
System Test
PCB Architecture
PCB Circuits
PCB Physical Design
PCB Fabrication
Design and Test Development
Customer
Validate
Verify
Post Silicon Verification
Test
Test

## Slide 3: Post-Silicon Verification
AFTER fabrication, make sure you built it right
  Find BUGS, not DEFECTS
  Identify problem of bug and determine a fix
Test in context, prevent bugs from going to field
  Issues often from design interacting with electrical conditions
Steps:
  Detect problem
  Localize problem (hardest part?)
  Find cause (Scan helps with this)
  Fix / bypass (survivability)
NB: ambiguity w/ verification vs validation

## Slide 4: Post-Silicon Verification
Challenges: complex chips, short schedules, complicated designs, diverse techniques
Pros: at speed (OoM faster); real system (no model error); real context
Cons: less controllability, observability; costly equipment, techniques (eg, BIST);
NB: ambiguity w/ verification vs validation

## Slide 5: Approaches
Design in features
Better pre-Si verification; emulation; esp. IO and mixed signal; CANNOT SEPARATE PRE- / POST-SI
Build tools for post-Si verification; EDA is key
  The new EDA challenge??
Formal (standardized?) interfaces
Formal coverage methods; assertions
SW: e.g. trace analysis, QED
Codesign verification/test with survivability
Instruction Footprint Recording (HW or SW)
Error resilience

## Slide 6: Challenges for Post-Si Verification
Long error detection latency (e.g. delay bw error occurrence and error detection)  need faster solutions
HW solutions require a priori design  SW solutions can retrofit
Low bug coverage  need to define, increase
Failure reproduction
How do you know you’re done?

## Slide 7: QED observations
Some bugs arise from multiple instructions in processor
Some bugs arise across multiple instructions outside processor, in uncore
Bugs affected by random events: electrical activity, asynchronous triggers, etc.
Augmenting code for validation can obscure the bugs (intrusiveness)
Conventional methods can take Billions of cycles to identify bug events

## Slide 8: Example:
Accesses to memory locations A and B end up creating error in cached C
Self checking A,B doesn’t find it
Long latency to find it
[1] Lin et al, TCADICS’14

## Slide 9: QED principles / techniques
Start with existing tests and transform them to improve bug detection
Trade-off detection latency and intrusiveness
EDDI-V:
  Why? Find bugs in processor core
  How? Replicate code blocks and run both copies
  Principle?
  Tradeoff: different lengths of instruction list

## Slide 10: QED principles / techniques (2)
PLC:
  Why? Find bugs in uncore
  How? Loads/consistency checks on variables from all threads
  Principle?
  Tradeoff: different lengths of instructions bw checks; different numbers of variables checked
CFCSS-V / CFTSS-V:
  Why? Find bugs in control flow
  How? Confirm flow of instruction blocks matches intent
  Principle?
  Tradeoff: different lengths of instructions bw checks

## Slide 11: CFCSS from [2]
“Map” flow of code blocks; generate signatures for each block; store those signatures and check at runtime
[2] Oh et al, ITR’02

## Slide 12: QED in action
Multicore with bug: deadlock – no execution
  Before: 10s watchdog timer: ~15B cycles
    Is this a fair base case?
  After: locate code causing bug after ~9-14 cycles
    How was it located? Deadlock stops function….
  “measured” intrusiveness with EDDI-V

## Slide 13: QED in action (2)
Sims on multicore with 80 bug classes, 1368 logic bug scenarios
  QED catches bugs way earlier!
    Runtime is way longer (Table IV) by 32000X
    Detect ALL bugs from original tests
    Detect up to 2X MORE bugs than original tests
Intel HW
  Similar results, 2X slower tests
Orthogonal to other techniques!
[1] Lin et al, TCADICS’14

## Slide 14: [3] Delay modeling
Model captures delay bounds; used for timing closure in design; pre-Si verification;
Delay testing: measuring delays on paths in Si
Post-Si testing intimately tied to pre-Si models: identify paths, generate vectors, analyze vectors
[3]: Problem: near / sub VT delay variation, poorly modeled. Multiple input switching (MIS) effect of 30-40% is ignored.

## Slide 15: Modeling Approach
Simulate “all” effects, generate characteristic curves, simplify curves (e.g. to PWL), create bounds, trim stored points
Principles: SIMPLIFY
[3] Das et al, ICCD’13

## Slide 16: Conclusion
Post-Si verification is critical but tricky
Ad hoc approach can work, but very costly
Make use of solid verification principles to get best results
QED techniques are effective for multicore SOCs, relatively easy to implement in code

## Slide 17: Discussion questions
How does the concept of fault coverage relate to the QED techniques?
For each of EDDI-V, PLC, CFxSS-V, what underlying principles are at work? What are alternative ways to apply those principles?
How does SoC testing differ from testing a monolithic circuit?
in [1] section V.A, how does the new test determine deadlock if no additional instructions are run beyond deadlock?
Writing: how could the order of the paper be changed to improve the paper?

## Slide 18: Bonus Discussion Questions
Are there HW equivalents to QED methods?
Were the results for QED convincing?

## Slide 19: Papers
[1] Lin, D.; Hong, T.; Yanjing Li; Eswaran, S.; Kumar, S.; Fallah, F.; Hakim, N.; Gardner, D.S.; Mitra, S., "Effective Post-Silicon Validation of System-on-Chips Using Quick Error Detection," Computer-Aided Design of Integrated Circuits and Systems, IEEE Transactions on , vol.33, no.10, pp.1573,1590, Oct. 2014.
[2] Oh, N.; Shirvani, P.P.; McCluskey, E.J., "Control-flow checking by software signatures," Reliability, IEEE Transactions on , vol.51, no.1, pp.111,122, Mar 2002.
[3] Das, P.; Gupta, S.K., "Gate delay modeling for pre- and post-silicon timing related tasks for ultra-low power CMOS circuits," Computer Design (ICCD), 2013 IEEE 31st International Conference on , vol., no., pp.227,234, 6-9 Oct. 2013.
[4] Keshava, J.; Hakim, N.; Prudvi, C., "Post-silicon validation challenges: How EDA and academia can help," Design Automation Conference (DAC), 2010 47th ACM/IEEE , vol., no., pp.3,7, 13-18 June 2010.
[5] Mitra, S.; Seshia, S.A.; Nicolici, N., "Post-silicon validation opportunities, challenges and recent advances," Design Automation Conference (DAC), 2010 47th ACM/IEEE , vol., no., pp.12,17, 13-18 June 2010.

## Slide 20: Paper Map
[1] Lin, D.; …"Effective Post-Silicon Validation of …," ICASICS’14.
[2] Oh, N.; …"Control-flow checking by software …," ITR’02.
[3] Das, P.; …"Gate delay modeling for pre- and …," ICCD’13.
[4] Keshava, J.; … "Post-silicon validation challenges: …” DAC’10.
[5] Mitra, S.; … "Post-silicon validation …," DAC’10.
[4] and [5] are broad, foundational reviews of the post-Si verification topic area
[2] is 1st work on control flow checking
[1] summary work on QED (2 prior conf pprs)
[3] 1st work on alternative post-Si method
One approach: SW method
Alternative approach: modeling method
[1] builds on [2] for 1 technique

## Slide 21: Glossary
Blocking bug: prevents testing/discovery of further issues
Electrical bugs: from electrical state – subtle
Intrusiveness: test changes design so as to obscure/prevent the original bug
Logic bugs: from design errors
Survivability features: ways to fix bugs post fab; chicken switches, µcode updates, fuses, etc.
Uncore: anything that is not processor